MAX6675	GPIO: MAX6675	0.1	GPL2	DAQ.tmplb_LowDevLib	en	Arcadiy Kisel
Cold-Junction-Compensated K-Thermocouple-to-Digital Converter (0°C to +1024°C). The module designed for the sensors connect throw softSPI by GPIO, mostly it's Raspberry PI BCM2835 GPIO. Conditions: Exclusively realtime planing in the priority 199 (FIFO-99). Template parameters: / Identifier Parameter Type Mode Attribute Configuration Value / addr GPIO address with functions mode(), get() and put(), mostly it's BCM2835 String Input Not attribute Constant DAQ.GPIO.io.pi / pin_cs pin_cs pin number of the GPIO Integer Input Not attribute Constant 8 / pin_sclk pin_sclk pin number of the GPIO Integer Input Not attribute Constant 11 / pin_miso pin_miso pin number of the GPIO Integer Input Not attribute Constant 9 / t T, °С Real Input Read only Variable / f_frq Function calculate frequency (Hz) Real Input Not attribute Variable 1000 / f_start Function start flag Boolean Input Not attribute Variable 0 / f_stop Function stop flag Boolean Input Not attribute Variable 0 / f_err Function error String Input Not attribute Variable 0 / Using/configuring: / 1. Create an output controller and a parameter object into the DAQ module "BCM 2835", by default it's "pi.pi". / 2. Create and start a logical controller object or use any presented one with the needed scheduling properties (FIFO-199). / 3. Create a logical parameter object and select the template for that, one for each sensor. (SCLK, MOSI may be common, CS must be independent) Enable the parameter. / 4. Into the tab "Template configuration" of the logical parameter object you need to set: / addr — to the address of the "BCM 2835" parameter like "DAQ.GPIO.io.pi"; tracing for the address changing is supported; / pin_cs — pin_cs pin number where connected the data pin of the sensor; / pin_sclk — pin_sclk pin number where connected the data pin of the sensor; / pin_miso — pin_cs pin number where connected the data pin of the sensor. / 5. Result: The logical parameter object will perform interaction and placing of gathered data to the Temperature attribute.